## Slide 1
Development of 241Am13C Calibration Source for a Large Water Cherenkov Detector
Colton Graham
PhD Candidate, University of Michigan
K. Ogren, Los Alamos National Lab S. A. Dazeley, Lawrence Livermore National Lab
M. Malek, University of Sheffield I. Jovanovic , University of Michigan
2023 MTV Workshop
March 22, 2023

## Slide 2: Water Cherenkov Detectors for Antineutrinos
Y. Schnellbach et al., arXiv:2301.08079 (2023)
Representative detector design
Inverse beta decay (IBD)
Neutron capture on Gd
Detection process for electron antineutrino in Gd doped water
Gd neutron capture de-excitation spectrum
Tanaka, Tomoyuki et al.
Progress of Theoretical and Experimental Physics (2019)
WATer CHerenkov Monitor for ANtineutrinos (WATCHMAN)
Kiloton gadolinium doped water based detector
Detection of antineutrinos by inverse beta decay (IBD)
Problem of energy calibration requires custom designs
M. Malek, University of Sheffield

## Slide 3: Calibration of Water Cherenkov Detectors
Electroplating substrate
Alpha source (241Am, 210Po)
Thin layer of 13C
Copper substrate
Source ON
Source OFF
Proposed source geometry
Branching ratio for 13C (α,n)
α energy threshold for γ ray production
P. Mohr, Phys. Rev. C 97 064613 (2018)
Monoenergetic high energy gamma ray source
Avoids neutron generator by use of radioisotopes
Ability to actively turn on and off
Correlated particle emission for background rejection
I. J. Arnquist et al., Phys. Rev. C 105 064610 (2022)
13C(α,n)16O
Emission of 6.1 MeV γ with correlated 1n

## Slide 4: Mission Relevance
Large antineutrino detectors offer prospects for nonintrusive far-field reactor monitoring
Remote detection of reactor operations inconsistent with declarations
Detection of undeclared reactors
A. Allega et al., Phys. Rev. Lett. 130, 091801 (2023)
Detection of aggregate reactor antineutrino signal in pure water from weighted mean distance of 650 km in 190 days
Simulated WATCHMAN sensitivity for 150 km standoff
L. Kneale et al., arXiv:2210.11224
Simulated WATCHMAN sensitivity for 1 month dwell time
O. Akindele et al., arXiv:2210.09391

## Slide 5: Simulation Models Disagree in Source Emission
Branching ratio of gamma ray to neutron emission from 241Am13C source
Gamma ray yield for 241Am13C source
Geant4 10.06 and FLUKA show discrepancy with initial α energy branching ratio
Branching ratio
Suggested source design relies on thin, difficult to manufacture geometry, necessitating use of simulation to optimize source before construction
Simulation with common radiation transport codes (Geant4, FLUKA) yields unphysical gamma ray to neutron production ratio
Motivates combination of new modeling and experiment to resolve discrepancies
Alpha source internal energy loss
γ ray production threshold

## Slide 6: Alpha Particle Transport Model
Initial energy
End of geometry element (Or E=0)
Measurement point of stopping power
Measurement point of cross section
Energy space
Energy ranges
R0
R1
R2
R3
R4
R5
R6
R7
R8
R9
R10
R11
R12
Geometry handled by particle ray tracing
Approximation yields analytical expression for interaction probability within energy range
Approximations
  Neglect energy and range straggling
  Assume alpha particle travel in straight line
  Does not model secondary particle emission and transport (e.g. delta rays)

## Slide 7: Source Optimization via Simulation
Uncorrelated neutrons
γ ray correlated neutrons
Simulated neutron spectrum from 241Am13C source
γ ray yield with alpha source thickness
Rapid fall off with thickness
γ ray yield with thickness of air between actinide and graphite source components
Yield quickly falls off, confirming ability to turn off source by simply moving components apart

## Slide 8: Validation of Simulation Methods
Comparison with traditional actinide beryllium neutron source
  Common commercial neutron source
  Neutron yield and spectrum characterized in literature
Source modeled as simple sphere of Be metal with homogeneously dispersed alpha source
Reasonable agreement of simulation code with literature data
Increases confidence in 241Am13C simulation
K. W. Geiger and L. Van der Zwan, Nucl. Instr. and Meth. 131 (1975) 315
Yield of homogenous α-Be source

## Slide 9: Expected Impact
Enabling technology for calibrating large water Cherenkov antineutrino detectors
Prototype calibration source of immediate interest for multiple prototype detectors under study
  UK BUTTON project
  LLNL prototype detector
  LBNL prototype detector
  BNL prototype detector
  Future full scale demonstrator experiment

## Slide 10: MTV Impact
Support for conference presentations to publicize work
  MTV Workshop 2022
  UPR Workshop 2022
  IEEE NSS-MIC-RTSD 2022
  MTV Workshop 2023
Facilitating national lab collaboration on source development
  Collaboration with Dr. Steven Dazeley at LLNL for source design
  Discussion with ORNL for actinide deposition
Transitioning technology for use in future detectors
  Fabrication underway for calibration source prototype

## Slide 11: Conclusions
Determined optimized geometry for 241Am13C calibration source
  Maximize yield of 6.1 MeV γ rays
  Minimize yield of uncorrelated neutrons
Developed custom heavy charged particle transport code to predict source yield
Simulated source yield to compare against measured signal of prototype source for verification

## Slide 12: Next Steps: Source Manufacturing Underway
Carbon deposition on copper foil underway at Pennsylvania State University Material Research Institute
  Deposition by 13C enriched methane
241Am deposition underway at University of Cincinnati
  Deposition of americium in nitric acid and isopropyl alcohol solution demonstrated on SiC Schottky diode
C. Dong, Pennsylvania State University
.Copper foil .without carbon.
.Copper with. .carbon deposition.
Hoffman, M.K. et al. J Radioanal Nucl Chem 331, 5423–5431 (2022).
Copper foil showing discoloration from carbon
Americium deposition scheme

## Slide 13: Acknowledgements
The Consortium for Monitoring, Technology, and Verification would like to thank the DOE-NNSA for the continued support of these research activities.
  This work was funded by the Consortium for Monitoring, Technology, and Verification under Department of Energy National Nuclear Security Administration award number DE-NA0003920. This material is based upon work supported under an Integrated University Program Graduate Fellowship. Any opinions, findings, conclusions or recommendations expressed in this publication are those of the author(s) and do not necessarily reflect the views of the Department of Energy Office of Nuclear Energy.