## Slide 1
Measurement of 9Be(ɑ,n) Cross Section for Safeguards Applications
Colton Graham
Graduate Student, University of Michigan
Jason Nattress1, Igor Jovanovic2
1Oak Ridge National Laboratory
2University of Michigan
2024 MTV Workshop
March 26th, 2024

## Slide 2: 9Be(ɑ,n) is an Important Nuclear Reaction for Safeguards Measurements
Be contaminant produces (α,n) backgrounds
  Pu/U α decay chains up to ~8 MeV
Safeguarding Gen. IV Reactors (FLiBe molten salt)
Actinide-Be (AmBe, PuBe) neutron spectra
M. Hua, et al., Nuclear Science and Engineering, 194:2, 154-162, (2020)

## Slide 3: Existing 9Be(ɑ,n) Cross Section Data is Sparse & Contradictory for Alpha Energies over 5 MeV
Sparse total σ
Minimal data for higher energy states
Space angle data
Conflicting data
Conflicting data
Conflicting data
Lacking data

## Slide 4: Measurement Campaign Conducted at University of Notre Dame Accelerator Facility
HPGe for 4.4 MeV γ-ray
Be foil target (125 μm)
0°
20°
40°
60°
90°
110°
130°
150°
Institute for Structural and Nuclear Astrophysics Nuclear Science Laboratory
5U target line
https://isnap.nd.edu/

## Slide 5: Analysis Highlight: Genetic Algorithm Spectral Fitting

## Slide 6
Analysis Highlight: Energy Dependent PSD Gates
Traditional PSD
Energy Dependent PSD
Gamma 3σ
Neutron 3σ

## Slide 7
Analysis Highlight: Neutron Spectral Reconstruction
Light output convolution
MLEM
Iterative solution to spectral matrix equation
Detector response matrix
Iterative reconstructed spectrum
Measured spectrum
Measured light output spectrum
Detector response matrix
True neutron spectrum
9Be(α,n0)
9Be(α,n1)
C. Lawrence et al., NIMA, 759, 16-22 (2014)
B. Pehlivanovic et al., Radiation Measurements, 49, 109–114 (2013)

## Slide 8: MTV Facilitates National Laboratory Collaboration
Opportunity to intern at Oak Ridge National Laboratory
Collaboration generated directly by 2023 MTV Workshop!
2023 MTV Workshop

## Slide 9: Next Steps
Ongoing analysis of 9Be(α,n) cross section
  Monte Carlo simulations of neutron transport and room return
  Follow up measurements with 3He array for low energy neutron states
Safeguards application measurements
  Assay of SNM with varying Be content
  AmBe neutron spectrum measurement to validate cross section data
Prototype Geant4 simulation model

## Slide 10: Acknowledgements
The Consortium for Monitoring, Technology, and Verification would like to thank the DOE-NNSA for the continued support of these research activities.
  This work was funded by the Consortium for Monitoring, Technology, and Verification under Department of Energy National Nuclear Security Administration award number DE-NA0003920