## Slide 1
Leakage Multiplication and Spontaneous Fission Source Strength Estimation Using Non-Point Model Factorial Moments
Jawad R. Moussa
Ph.D. Student, University of New Mexico
Advisor: Anil K. Prinja University of New Mexico
2024 MTV Workshop
March 26th, 2024

## Slide 2: Introduction and Motivation
The rapid characterization of special nuclear material is central to the NNSA safeguards and nonproliferation mission
  Nondestructive Assay techniques such as Neutron Multiplicity Counting (NMC) and Gamma Spectroscopy are commonly used
NMC is based on measuring the time series of neutron detection events to infer physical properties of the sample
\
We leverage our deterministic implementation of NMC moments in LANL’s PARTISN code to assess the accuracy of the point kinetic model (PKM)
=
Machine learning models are used to infer sample characteristics from factorial moments for increased accuracy over PKMs
Monte Carlo
Deterministic
Point Kinetic Models

## Slide 3: & Estimation with Non-point Moments
Leakage Multiplication the number of neutrons leaking from the system per initial source particle
Three configurations of the BeRP ball were simulated
  Bare metal sphere
  Metal sphere moderated by 1-inch HDPE
  Metal sphere reflected by 1-inch Cu
Derived a set of point kinetic model (PKM) equations relating factorial moments to and
  Consistent with the equations implemented in PARTISN
Figure 2. Various configurations of the LANL BeRP ball illustrating the models simulated for analysis

## Slide 4: PKM Estimation of &
 | Bare BeRP | 1in HDPE | 1in Cu
MCNP F1 Tally | 3.05 | 5.06 | 5.09
Moment Estimate | 3.32 | 4.25 | 5.51
Error | 8.85% | 16.00% | 8.25%
 | Bare BeRP | 1in HDPE | 1in Cu
PARTISN Input | 28.19 | 28.19 | 28.19
Moment Estimate | 25.69 | 24.17 | 25.93
Error | 8.88% | 14.25% | 8.02%
True leakage multiplication () was estimated from MCNP using a fixed source F1 tally
True spontaneous fission source strength () was obtained from PARTISN input data
Table 1. estimation of various BeRP ball configurations using non-point moments with PKM equations
Table 2. estimation of various BeRP ball configurations using non-point moments with PKM equations

## Slide 5: Can we improve on the point model?
The inverse problem is complex, but deterministic approaches for computing NMC moments are efficient and computationally inexpensive
Can machine learning (ML) be leveraged to help address this challenge?
A workflow was developed to generate a dataset for ML training and testing
  Three BeRP ball configurations (Bare, 1in HDPE, 1in Cu)
  BeRP ball radius is parameterized to achieve various multiplications
  True BeRP ball radius was not included in dataset
Various regression algorithms were explored (ex. linear regression, polynomial regression, K-nearest neighbor and decision tree)
Generate PARTISN input files
Generate slurm submission scripts
Submit to HPC
Compute NMC Moments
Extracts moments from outputs
Generate dataset and train ML model
Predict ML and F from moments
PARTISN Input Template
Bash
PARTISN
Python

## Slide 6: Machine Learning Model Estimation of &
 | Bare BeRP | 1in HDPE | 1in Cu | 80% 239Pu 20% 240Pu
MCNP F1 Tally | 3.05 | 5.06 | 5.09 | 2.77
PKM Estimate | 3.32 | 4.25 | 5.51 | 3.13
DT Prediction | 3.08 | 4.77 | 5.21 | 2.44
 | Bare BeRP | 1in HDPE | 1in Cu | 80% 239Pu 20% 240Pu
PARTISN Input | 28.19 | 28.19 | 28.19 | 93.70
PKM Estimate | 25.69 | 24.17 | 25.93 | 83.32
DT Prediction | 28.33 | 28.33 | 28.33 | 139.39
Table 3. 4 moment estimation for various Pu samples using a decision tree model trained on BeRP ball data
Table 4. 4 moment estimation for various Pu samples using a decision tree model trained on BeRP ball data

## Slide 7: Decision Tree Algorithm Performance
Chart: % Error in ML Prediction
| Bare BeRP Only Dataset | 1in HDPE Only Dataset | 1in Cu Only Dataset
Bare BeRP Configuration | 0.98361 | 18.3607 | 7.8689
1in HDPE Configuration | 56.917 | 5.7312 | 51.7787
1in Cu Configuration | 28.8802 | 63.0648 | 2.3576
Figure 3. 2 moment estimate of for various BeRP ball configurations using a DT model trained on model specific datasets
Figure 4. 4 moment estimate of for various BeRP ball configurations using a DT model trained model specific datasets
Chart: 
| Bare BeRP Only Dataset | 1in HDPE Only Dataset | 1in Cu Only Dataset
Bare BeRP Configuration | 0.98361 | 10.8197 | 0.98361
1in HDPE Configuration | 13.6364 | 5.7312 | 20.5534
1in Cu Configuration | 14.1454 | 7.8585 | 2.3576

## Slide 8: Can we infer more than just & ?
A classification model was trained to distinguish between bare samples and predict moderator type
Various classification algorithms were explored (ex. Decision tree classifier, Support Vector Machine, k-Nearest Neighbor, and Gaussian Naive Bayes)
Generalizations:
  Fissile vs. nonfissile distinction
  Moderator thickness prediction
  Feature importance
 | DT Classifier | KNN Classifier
Bare BeRP | Bare | Bare
1in HDPE | HDPE | HDPE
1in Cu | Cu | Cu
Bare 80-20 239Pu:240Pu | Cu | Bare
 | DT Accuracy | KNN Accuracy
Training set | 100% | 100%
Testing set | 100% | 96%
Table 5. Reflector type prediction and model accuracy for two ML classification models

## Slide 9: Expected Impact & MTV Impact
The capability to deterministically compute full phase space moments of the neutron count distribution extends existing NMC modeling capabilities
Using ML to infer sample characteristics adds to the arsenal of safeguards and nonproliferation tools and analysis techniques
MTV as facilitated collaborations with LANL
  NEN-2: MCNP Modeling
  CCS-2: Deterministic Modeling (PARTISN)
  XCP-3: PARTISN/MCNP Comparison
LANL Collaborators: Jesson Hutchinson, Nathan Hart, and Erin Davis

## Slide 10: Conclusions
Point model predictions of & worsen for heterogenous samples
  Estimation is strongly dependent on the accuracy of 1-group data representations
The PARTISN implementation of NMC moments enables the rapid generation of datasets
ML models show great potential for estimating & with improved accuracy over the PKM in addition to predicting sample characteristics not previously accessible
ML approaches require further exploration for practical nonproliferation applications
  Optimization is key!

## Slide 11: Acknowledgements
The Consortium for Monitoring, Technology, and Verification would like to thank the DOE-NNSA for the continued support of these research activities.
  This work was funded by the Consortium for Monitoring, Technology, and Verification under Department of Energy National Nuclear Security Administration award number DE-NA0003920