## Slide 1
Neutron Signatures for Nondestructive Assay in Thorium Fuel Cycles
Oskar Searfus
Ph.D. Candidate, University of Michigan
Peter Marleau2, Heather Reedy2, and Igor Jovanovic1
1University of Michigan
2Sandia National Laboratories
2024 MTV Workshop
March 26, 2024

## Slide 2
Intro: the Thorium Fuel Cycle
232Th used as fertile isotope:
Minimal transuranic production
Th more abundant than U
Breeding possible with thermal reactor
Th fuel cycle already commercially demonstrated
India: FBTR in operation, more reactors planned
China: TMSR construction complete, startup imminent
Export of these technologies to NPT signatory non-nuclear weapon states possible, but safeguards will be required

## Slide 3: Mission Relevance: Challenges in Safeguarding 233U
2.6 MeV γ
IAEA sets conservative significant quantity (SQ) for 233U
8 kg for 233U vs. 25 kg for 235U
Th fuel cycle designs – 233U/235U mixtures
233U & 235U must be quantified separately
232U contaminates 233U
Produced in (n,2n) reactions
Typical concentration ~100-2000 ppm U
208Tl decay → 2.6 MeV γ: extreme γ environment – 6.04 Ci/SQ @ 100 ppm:

## Slide 4: Technical Approach: Candidate Neutron Signatures of 233U
Delayed neutron time profile: isotope-specific
Differential die-away:
Indicates fissile material
Fast neutron spectroscopy:
Distinguish between fission & non-fission neutrons
Simulation (4He detector)

## Slide 5: Selection of Detectors
Arktis S670 4He detector
Insensitive to γ-rays
Sensitive to neutron spectrum
MC-15 3He detectors
Insensitive to γ-rays
High-efficiency thermal neutron detector

## Slide 6: Experimental Overview
Thermo Scientific P211 D-T generator
AT-400R container: 36 Zero Power Reactor (ZPR) plates, 33 g 233U3O8 / plate; lined with 1.25” lead
1 x Arktis S670 4He fast neutron detector1
2 x MC-15 3He thermal neutron detectors
1O. F. Searfus, K. Ogren, and I. Jovanovic, NIM A 1046, 167703 (2023)
Measurement performed at the National Criticality Experiments Research Center (NCERC):
Nuclear material repository @ Nevada National Security Site (NNSS)

## Slide 7: Material Composition & γ-ray Environment

## Slide 8: Results: Passive Neutron Spectral Signature
O(⍺,n) neutrons spectrally distinct from fission neutrons
induced/spontaneous fission fraction
(⍺,n) fraction

## Slide 9: Results: Differential Die-Away
Measured time constant for DDA consistent with simulated time constant
Potential unique capability of 4He detector: other fast neutron detectors inoperable in intense γ environment (70 mR/hr)

## Slide 10: Results: Delayed Neutrons
MC-15 measured & simulated delayed neutrons are good fit to tabular 6-group DN parameters.
Fitting parameters:
scaling factor (C)
flat background (B)
Methodology previously demonstrated for 235U / 238U:
J. Nattress et al., Phys. Rev. Applied 10, 024049 (2018)
K. Ogren et al., Phys. Rev. Applied 14, 014033 (2020)
measurement
simulation

## Slide 11: Expected Impact
This work is the first demonstration of nontraditional neutron signature measurements on 233U
These signatures can now serve as a benchmark for future nondestructive assay technology developments for emerging thorium fuel cycles
Since traditional safeguards technology may not be appropriate for thorium fuel cycles, the findings of this work address a key challenge for the international safeguards portfolio

## Slide 12: MTV Impact
MTV helped connect me with my current colleagues at Sandia National Laboratories, and support the experimental research efforts for my Ph.D.
SNL Collaborators:
  Pete Marleau, Heather Reedy, Scott Kiff, and others.
I will be transitioning to staff at SNL in April
Technology transitions
  ESARDA nondestructive assay working group meeting in May
  Past collaborations with ORNL
  Plan to disseminate project findings to IAEA and EURATOM

## Slide 13: Conclusion
I demonstrated a proof-of-concept for three novel neutron signatures of 233U, taking the first step toward safeguards technology for thorium fuel cycles.
This work was recently published:
  O. Searfus, P. Marleau, E. Uribe, H. Reedy, and I. Jovanovic, “Passive and active neutron signatures of 233U for nondestructive assay,” PRApplied 20 6 064038 (2023) doi.org/10.1103/PhysRevApplied.20.064038

## Slide 14: Next Steps: Delayed Neutron Isotope Ratio
Experiment recently performed at Oak Ridge National Laboratory
Delayed neutrons from 233U/235U mixed isotope items measured with modified active well counter
Measure 233U/235U ratio nondestructively by quantifying shape of DN time profile

## Slide 15: Acknowledgements
The Consortium for Monitoring, Technology, and Verification would like to thank the DOE-NNSA for the continued support of these research activities. The work of O. Searfus was performed under appointment to the Nuclear Nonproliferation International Safeguards Fellowship Program sponsored by the National Nuclear Security Administration’s Office of International Nuclear Safeguards (NA-241). Sandia National Laboratories is a multimission laboratory managed and operated by National Technology Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE NA0003525. The National Criticality Experiments Research Center is supported by the DOE Nuclear Criticality Safety Program, funded and managed by the National Nuclear Security Administration. This work was funded by the Consortium for Monitoring, Technology, and Verification under Department of Energy National Nuclear Security Administration award number DE-NA0003920